## Slide 1
HS&E INCIDENT BULLETIN |  | 2nd Quarter 2013 | 
U.S.A. | Type of incident Fall of Material |  | 
Summary: |  | 
While removing a bearing case support spring with a pry bar the individual lost his footing. The result was the pry bar falling from as the assembler went to catch himself. The pry bar then hit his co-worker in the left eye. |  | 
Root Causes: | Actions Taken Thus Far: Next Steps | 
Failure to maintain most current issue of tooling. Employee in the line of fire Failure to provide stable work platform | Restrict area around work space during this operation Review Spring location Review tooling used to perform the operation to create alternative for pry bar. Establish work platform minimum expectations | 
Pry Bar Inserted in spring to remove Coupling.